## Slide 1: Carbon-Free Electricity Policies Impacts & Perspectives
Your Trusted Energy Partner
Rick Dunn, General Manager/CEO
October 29, 2024
Fall Economic Forecast Meeting

## Slide 2: rickdunn.substack.com
Began Publishing November 2023
Optional & Free to Subscribe
Artistic Collaboration: Marjean Allen-Dunn
https://rickdunn.substack.com/

## Slide 3: Agenda
Northwest Close to Blackouts – How did we get here?
WA & OR Clean Energy Policies – Global & U.S. Perspectives
WA Energy Strategy – We’re Coming for Your Wind MT & WY!
Where Do We Go from Here? – Near and Long Term

## Slide 4: Northwest Close to Blackouts
Northwest Imported Electricity for all 120 Hours of Cold Snap
Hydro short on water, natural gas maxed out & wind power collapsed to zero
+2,000 MW of coal retirements so far
Demand grew 2% to 6% since December 2022 winter event
Northwest electric grid & natural gas pipeline systems are at immediate risk with no margin for the unexpected
January 12 – 16, 2024
No Net Energy from California Generation
Nuclear, Natural Gas & Coal Imports
Multiple Utilities Declared Energy Emergencies

## Slide 5: Northwest has Long Exported Electricity to California
Pacific HVDC South Terminal near Los Angeles
Pacific Interties went into service 1968 - 1970
Path for Hydropower surpluses in the Northwest to flow to California
High Voltage Direct Current (DC) allows more precise control of power flow and lower losses; but more complicated
Canada & Montana Interconnections becoming more important
Western Interconnection
Transmission Lines
Pacific
DC & AC Interties
8,000 MW
Pacific HVDC North Terminal near The Dalles
U.S. – Canada Interconnections
Montana – Colstrip

## Slide 6: Northwest Beginning to Import Electricity via CA
Graphs below zero indicate flows from CA to NW
January 2024 Cold Weather Event
DC Line Outage for Maintenance

## Slide 7: Power Grid Basics: A Service Like No Other!
Electricity is simultaneously:
Produced
Delivered
Consumed

## Slide 8: Alternating Current (AC) Electricity
Three-Phase Requires 3 Wires
60 cycles per second sine waves
All Generators must be Synchronized
Increasing Demand Tends to Decrease Speed of Rotation
Decreasing Demand tends to Increase Speed of Rotation
N
S
Speed of rotation precisely controlled
Rotating Magnetic Field

## Slide 9: Demand/Supply Balancing: Physics
Electrical Demand and Supply Must Be Equal at All Times
‘Cruise Control’ set at 60
  No over supply
  No under supply
The Laws of Power Grid Physics are Unforgiving
Consequences of not maintaining supply & demand balance are blackouts
60 cycles per second
Notes: 4,000 MW OF FIRM GENERATION IS BEING RETIRED IN THE NWPP. THERE IS NO ORGANIZATION IN THE NORTHWESTERN UNITED STATES RESPONSIBLE FOR RESOURCE ADEQUACY PLANNING
ONLY RELIABILITY REQUIREMENTS ARE OPERATIONAL
ANTI FOSSIL FUEL AND ANTI NUCLEAR SENTIMENT COMBINED WITH STRONG WIND AND SOLAR POWER ADVOCACY HAS PUSHED UTILITIES INTO A GAME OF CHICKEN.

## Slide 10: Controllable Supply: Blackout Insurance
Uncontrollable Low
Effective Capacity
Controllable
High
Effective Capacity
Effective Capacity = % of Installed Nameplate Generation that can be Counted on During Hours of Maximum Demand
Coal & Natural Gas
50% of Effective Capacity
Hydro
40% of Effective Capacity

## Slide 11: Coal = 16% of U.S. Electricity
NW Coal Plant Closures
Colstrip(1) 716 MW in 2019
Centralia(1) 730 MW in 2020
Boardman 600 MW in 2020
Centralia(2) 730 MW in 2025
2,776 MW by 2025
+3,000 MW more in ?
Source: epa.gov/egrid/data-explorer
Total generation (MWh)
by plant
Coal =12% of PNW

## Slide 12: Natural Gas = 43% of U.S. Electricity
Source: epa.gov/egrid/data-explorer
Total generation (MWh)
by plant
Natural Gas 23% of PNW
5,000 MW
Interstate-5
Population Centers
100% CO2-Free Policy Impacts?
Controllable
&
Power/Energy
Dense
High MW/MWh
Per Acre

## Slide 13: U.S. Electricity: Coal to Natural Gas Fuel Switching
36% CO2 Reduction
Down 869 MMT since 2005
Natural Gas
50 to 60% less CO2 than Coal
Plus, Wind & Solar
Emissions Trending Downward
https://www.epa.gov/ghgemissions/inventory-us-greenhouse-gas-emissions-and-sinks-1990-2022
Electricity Generation Flattened

## Slide 14: Hydropower = 5.7% of U.S. Electricity
Source: epa.gov/egrid/data-explorer
Total generation (MWh)
by plant
Northwest Hydropower Like Nowhere Else:
Electricity Provided
50% of PNW Region
60% of Washington
Hydro-Based
100% CO2-Free Electricity does not scale to the rest of the U.S.

## Slide 15: Nuclear = 18.6% of U.S. Electricity
Total generation (MWh)
by plant, 2022
Total generation (MWh)
by plant
Source: epa.gov/egrid/data-explorer
Nuclear
3% of PNW
Controllable
&
Power/Energy
Dense
High MW/MWh
Per Acre

## Slide 16: Wind = 10.2% of U.S. Electricity
Total generation (MWh)
by plant
Wind
10.5% of PNW
Source: epa.gov/egrid/data-explorer
Uncontrollable
&
Power/Energy
Dilute
Low MW/MWh
Per Acre

## Slide 17: Northwest Wind Power Effective Capacity
ELCC = Effective Load Carrying Capability
5.5%
Montana
30%
Overbuild Factor
+18,000 MW
of Washington Wind
Replaces only
1,000 MW
of January
100% Effective Capacity

## Slide 18: Solar = 3.9% of U.S. Electricity
Total generation (MWh)
by plant
Solar
0.9% of PNW
Source: epa.gov/egrid/data-explorer
Uncontrollable
&
Power/Energy
Dilute
Low MW/MWh
Per Acre

## Slide 19: Northwest Solar Power Effective Capacity
Northwest Solar Extremely Low Effective Capacity in Winter
ELCC = Effective Load Carrying Capability
2% to 3%

## Slide 20: NW Supply & Demand Balancing: January 2024 Cold Snap
38 Balancing Area Authorities in Western Power Grid
Maintain supply & demand balance including scheduled generation imports and exports
Expanded “Northwest” Footprint

## Slide 21: NW Electricity Demand: January 2024 Cold Snap
Electricity Demand Cold Winter Days January 2024
Daily Rhythm of Life
Demand Curve is Power & Must be Precisely Matched
  Controllable Effective Capacity
Area Under Curve is Energy
Note: y-axis is megawatt-hours (energy) per hour or average megawatts (power)

## Slide 22: NW Electricity Supply: January 2024 Cold Snap
Future Concerns with Shutting Down Coal & No New Natural Gas
More Dependence on Drought Susceptible Hydropower
Ecological & Financial Costs to Overbuild Wind & Solar
Increasingly Risky & Costly Probability Game
Wind & Solar are parasitic to the “reliable grid” – effectively negative demand
Wind Energy Drops by 94%
Solar 0% during hours of darkness
Note: y-axis is megawatt-hours (energy) per hour or average megawatts (power)
“Averages are the enemy of reliability planning” Randy Hardy

## Slide 23: NW Hydro: Flexes Polar Vortex Muscle
WA & OR Wind Power at Zero or Less During Coldest Temperatures
https://rickdunn.substack.com/p/northwest-hydro-flexes-its-polar

## Slide 24: Agenda
Northwest Close to Blackouts – How did we get here?
WA & OR Clean Energy Policies – Global & U.S. Perspectives
WA Energy Strategy – We’re Coming for Your Wind MT &WY!
Where Do We Go from Here? – Near and Long Term

## Slide 25: WA Clean Energy Transformation Act (CETA)
CETA Requirements
20% of utility portfolio can be CO2 emitting generation with offsets
Has effectively eliminated investment in new natural gas generation so far

## Slide 26: Oregon Clean Energy Bill
Directs two largest utilities to deliver 100% clean electricity to customers by 2040
Stairstep from 80% clean electricity by 2030, to 90% percent by 2035 and 100% by 2040
Prohibits new or expanded natural gas-fired power plants in the state (also illegal to build nuclear plants)
Most ambitious timetable in the nation

## Slide 27: Washington & Oregon: What Dirty Energy Problem?
Source: https://www.epa.gov/egrid/data-explorer
% of U.S. Total (1,745 MMT)
WA = 10.8 MMT (0.62%)
OR = 9.13 MMT (0.52%)
Hydropower Like Nowhere Else
Idaho = 2 MMT (0.1%)

## Slide 28: CO2 Reductions: Local versus Global
“…cuts are necessary to prevent the worst effects of climate change on our state’s coastlines, water supplies, forests, environment, and economy.”
https://ecology.wa.gov/air-climate/reducing-greenhouse-gas-emissions/tracking-greenhouse-gases/ghg-inventories
Electricity ≈ 11 MMT
What the rest of the world is doing matters & says something
Extent & rate of CO2 reductions
  Virtue signaling vs. global impacts
  Bending the Curve vs. Going Over a Cliff
  Grid Reliability Risk
  Increasing Energy Rates
  Land-use Impacts
Total Energy ≈ 74 MMT
Poor Hydro Year & Includes “Other”
US EIA 2021 Data

## Slide 29: As We Push Grid to Blackout: Global CO2 Emissions Rise
Since 2007
U.S. decreased by 1,070 MMT
China increased by 4,420 MMT
China
2 new coal plants per week in 2022
In 2023, new coal plant construction hit an eight-year high.
11,400 MMT
+37,000 MMT per Year
5,060 MMT
Atmospheric CO2
420 ppm today (0.04%)
280 ppm pre-industry
<200 ppm some plants die
<150 ppm all plants die

## Slide 30: Rapid Global “Energy Transition” ?
5% Wind and solar
83% Fossil Fuels & Biomass
6.3% Hydro
3.8% Nuclear
Source: https://ourworldindata.org/energy-production-consumption
Electricity is 16% of Global Energy Consumed

## Slide 31: U.S. Total Energy Consumption in 2023
Fossil fuels = 83%
Wind & Solar = 2.6%
  Hydro = 0.9%
  Total Renewables = 9%
Nuclear = 9%
Electricity Represents 34% of total U.S. Energy
Wind was 18%x 9% =1.62% & Solar was 11%x9%=0.99%
Wind & Solar combined were 2.6% of U.S. primary energy consumption in 2023

## Slide 32: U.S. Electricity Generation
Fossil Fuels = 60%
Renewables = 21.4%
  Wind & Solar = 14.1%
  Hydro = 5.7%
Nuclear = 18.6%
39% Non-CO2 Emitting
Source: https://www.eia.gov/energyexplained/electricity/
84%
New Generation Under Development

## Slide 33: Agenda
Northwest Close to Blackouts – How did we get here?
WA & OR Clean Energy Policies – Global & U.S. Perspectives
WA Energy Strategy – We’re Coming for Your Wind MT & WY!
Where Do We Go from Here? – Near and Long Term

## Slide 34: We’re Coming for Your Wind MT & WY!
Washington State Energy Strategy
+10,000 aMW = 10 x Columbia Generating Station Nuclear Plant

## Slide 35: WA Energy Strategy: Everywhere but Here
63,000 MW onshore wind
+100 Seattle-sized farms
38,000 MW solar
+116 million panels
WA Wind = 2,000 MW

## Slide 36: Washington’s Vision for the Northwest
Total generation (MWh)
by plant
Source: epa.gov/egrid/data-explorer
Texas
+37,000 MW
Southwest Power Pool
+31,000 MW
WA Vision for NW
+63,000 MW

## Slide 37: Wind & Solar: Land Use Impacts
Assumes 100% of Existing Hydropower stays in Place
Transmission Lines Needed to Bring
Wind and Solar Power to Population Centers
Source: Public Generating Pool study by E3 Consulting submitted to WA State Legislature prior to passage of CETA

## Slide 38: Transmission Lines: Development & Operations Friction
High up front capital costs & long siting, permitting & construction lead times
  15 years or more not uncommon
Wildfire legal and financial risks
  Risk mitigation includes preemptive shutoffs and blackouts

## Slide 39: Boardman-to-Hemingway: Tx Line Case Study
300 miles
Need identified 2002
1,000 MW Capacity
Project defined 2006
Complete by 2026?
Raises serious questions about WA doubling electricity capacity and counting on Montana & Wyoming Wind
500 kilovolts
Idaho Power & PacifiCorp joint ownership
BPA not participating in construction or ownership

## Slide 40: Land-Use Conflicts: Development Friction
Source: https://www.americanexperiment.org/reports/not-in-our-backyard
Tally Of US Wind & Solar Rejections Hits 735 - Robert Bryce (substack.com)

## Slide 41: Not-In-My-Backyard: NIMBY Case Study
Benton County, Washington
Local Electricity > 95% CO2 Free Today
Developer bypassing “locals” using State EFSEC
850 MW Nameplate
280 avg MW
47 MW
January
Effective Capacity
Contribution
133% x Seattle Land Area
“communities and community members must have a seat at the table in designing programs and selecting projects.” WA 2021 State Energy Strategy
+200 Turbines up to 600 feet tall
112 square miles

## Slide 42: Endangered Species: Just Another NIMBY
Washington Department of Fish & Wildlife has identified “collision with wind turbines” as one of several direct sources of mortality
Nowhere to Hide

## Slide 43: Inflaming the Rural/Urban Divide: “Green Tyranny”
Step 1
Replace Environmentalism with Climatism
Wrecking the Planet to “Save It”
Step 2
Regulatory Reforms
Eminent Domain on Steroids
Step 3
Push the Grid to a Reliability Cliff
More wind & solar over a bigger area … and fast!
Step4
Propaganda
Our “bold actions” will change the future of the planet & there’s no price too high for others to pay
"You've got to break a few eggs to make an omelette".
https://rickdunn.substack.com/p/bold-action-or-green-tyranny

## Slide 44: Agenda
Northwest Close to Blackouts – How did we get here?
WA & OR Clean Energy Policies – Global & U.S. Perspectives
WA Energy Strategy – We’re Coming for Your Wind MT & WY!
Where Do We Go from Here? – Near and Long Term

## Slide 45: NW Utility Balancing Act: Becoming Increasingly Difficult
Reliable
Affordable
Environmentally Responsible
Electricity
Health, Safety & Well Being
Hydropower Erosion
  Increased spill & threats of dam breaching
Eliminating CO2 valued above all factors
  Coal-plant retirements & no new natural gas in WA & OR
Wind & Solar: Weather Dependent & Energy Dilute
  Located remotely from population centers & require vast swaths of land due to need for extreme overbuild
Increasing Costs & Risk of Blackouts

## Slide 46: Northwest Demand +30% in 10 Years
Winter & Summer Firm Peak Requirements
Could Increase Nearly 10,000 MW in 10 yrs
https://www.pnucc.org/system-planning/northwest-regional-forecast/

## Slide 47: Utility Forecasts: Highly Uncertain
Status Quo
High Electrification
Load Forecast Scenarios
Which is it?
What about Data Centers & other Electricity Intensive Loads?
Drives need for scalable, rapidly deployable, CO2-free, & reliable generation

## Slide 48: Pacific Northwest Generating Capacity Now & Possible Future
Source: https://www.nwcouncil.org/energy/energy-topics/power-supply
 | Average MW | Capacity Factor
Hydro | 16,271 | 47%
Natural Gas | 7,882 | 80%
Coal | 4,059 | 78%
Wind | 3,552 | 32%
Solar | 304 | 26%
Average Year Energy
WA & OR Vision
Eliminate
Natural Gas & Coal
-12,000 aMW
x2 Electrification
+16,000 aMW
Unprecedented Development in an Anti-Development Era
In 25 years construct +28,000 aMW
=100 years of Hydro, Natural Gas & Coal Development
Nameplate Capacity

## Slide 49: PNW Hydro is Great! But Highly Variable
+3,000 to +9,000 aMW
+4,000 to +7,000 aMW
https://www.bpa.gov/energy-and-services/power/resource-planning
Firm Generation Spoken For
Surplus May or May Not Show Up
3 to 9 X
CGS
Nuclear Plant
In Some Months

## Slide 50: BPA Transmission Lines: Critical to All Utilities
BPA Owns & Operates 75% of NW Grid
Source: BPA April 2023 Presentation “The Evolving Grid Update on the State of Transmission”

## Slide 51: BPA Transmission: Interconnection Frenzy
Generator Interconnection Requests
BPA hasn’t built significant new
transmission lines in decades
Transmission Interconnection Requests
300

## Slide 52: Land-Use vs. CO2 Footprint: Finding Common Ground
What if we built:
As Little Transmission as Absolutely Necessary
Reliable Generation Plants
  Small-footprint
  Low or no-CO2
  Closer to where people live
Natural gas is 100 to 1,000 X more power dense than wind and solar
New nuclear with safety perimeter at fence line will increase power density
Up to 60% less CO2 than coal

## Slide 53: Land-Use vs. CO2 Footprint: Finding Common Ground
Energy contained in a gummy bear pellet of uranium fuel
= 2,000 pounds of coal

## Slide 54: Small Footprint Nuclear: Long-Term Solution
1,000 aMW of wind power = 500 to 1,000 square miles of land
720 MW Small Modular Reactor Complex = 0.05 square miles of land
Source: https://www.americanexperiment.org/reports/not-in-our-backyard

## Slide 55: New Nuclear: Gaining Momentum
ARDP Grant Recipient #1
ARDP Grant Recipient #2
Advanced Reactor Demonstration Program

## Slide 56: New Nuclear: Gaining Momentum
ARDP Grant New Recipient #1
Breaking Ground in 2026
“completed by end of decade”
ARDP Grant Recipient #2
Breaking Ground Now
2030 Operational Goal

## Slide 57: Amazon Steps Up for Site-1 SMR!
57
Original ARDP Grant #1, now DOE Loan Program Office
Amazon to purchase first 4 modules
Energy Northwest has option to build additional 8 modules
Additional power available to Amazon and northwest utilities
4 Modules Initially with up to 12 Total
80 Megawatts per Module
On-Line Goal = Early 2030s

## Slide 58: Scalable, CO2-Free, Reliable & Safe
Walk-Away-Safe
Meltdown-Proof

## Slide 59: Benefits of zero-emitting firm capacity at 100% GHG reductions
$-1.4B
Adding
Avoids
+1.2 GW CGS
-9.5 GW Storage
-44.8 GW Wind
-37 GW Solar
+6.5 GW Firm
-91 GW Non-firm
CGS + NuScale SMRs reduce system costs by almost $8B per year relative to RE + Storage
100% GHG Reduction Portfolios
+5.3 GW SMRs
Avoids 80 to 150 Seattle-Sized Wind Farms & 112 M solar panels

## Slide 60: Data Centers: Need Baseload Generation Now
Big Tech’s “Dirty Little Secret”
Natural Gas Power + Renewable Energy Certificates
“Greenwashing”
Driving Nuclear Renaissance
https://rickdunn.substack.com/p/wind-and-solar-green-industry-fantasyland

## Slide 61: Natural Gas: Policies vs. Reality
How Natural Gas is Used in the Pacific Northwest
More than half of the total energy consumed in the region — either used directly for space and water heat or in industrial processes, or as gas-generated electricity. (Excludes transportation uses.)

## Slide 62: Natural Gas: We need you, but WA/OR policies hate you
replace decommissioned coal plant power
balance intermittent renewable sources
“The region’s existing storage assets would not be able to make up the 90-day capacity deficiency if the region experiences a cold winter.”
Pipeline Capacity Maxed Out
Increased NG electricity generation

## Slide 63: Capital Costs: Low & No-CO2 Emissions Generation
Combined-Cycle Natural Gas
$1.2 billion per 1,000 MW
Wind
$2.3 billion per 1,000 MW
Solar:
$1.4 billion per 1,000 MW
Costs: U.S. Energy Information Administration Northwest Power Pool 2022 $
Lithium-Ion Batteries
$1.3 billion per 1,000 MW
4-hour Discharge Duration
Increases Effective Capacity
Risk of Multi-day Energy Drain
High Capital $ Due to Overbuild

## Slide 64: Wind & Solar Grid Costs: Cautionary Tale from Germany
Residential/Industrial Avg. ¢ per kWh
  Germany: 40/26.4
  +39% wind& solar annual electricity
  De-industrialization is occurring
Germany leads on:
concentration of wind & solar per capita
Highest priced electricity
https://www.iea.org/countries/germany

## Slide 65: West Coast Residential Rates Increasing
West Coast Residential Rate Increases Since May 2019
WA/OR/CA = 12¢/15¢/34¢ per kWh
California +75% Increase
Oregon 34% Increase
Washington 24% Increase
CA is 280% x WA Rates
26% in-state wind & solar electricity

## Slide 66: West Coast Industrial Rates Increasing
WA/OR/CA = 6.4¢/7.6¢/26¢ per kWh
California +133% Increase
Oregon 36% Increase
Washington 42% Increase
West Coast Industrial Rate Increases Since Jan 2019
CA is 406% x WA Rates

## Slide 67: Unspoken Environmental Costs: Cradle-to-Grave
All energy conversion technologies involve Environmental Tradeoffs
Social cost of carbon should not be the only environmental metric

## Slide 68: Wind & Solar: Land & Mineral Intensive
500% to 1,800% Increase in Minerals per Watt of Electricity
IMF economists predict metal prices would reach historical peaks
“for an unprecedented, sustained period of roughly a decade.”

## Slide 69: Energy Transition: Mining Reality Check
Mining critically needed and OK
as long as it’s somewhere else
16 years to bring new mine into operation

## Slide 70: Wind & Solar: Increasing Cost Curves
Power Purchase Agreement (PPA) Pricing
Mark Mills Manhattan Institute: https://www.youtube.com/watch?v=sgOEGKDVvsg
Temporary or Permanent?

## Slide 71: Keep in Mind: It’s a Great Time to be Alive!
“We live longer, healthier, safer, wealthier, freer, more peaceful and more stimulating lives than those who came before us.”
Steven Pinker, Harvard Psychologist

## Slide 72: Conclusions: Ideas Worth Considering
Be wary of climate catastrophizing as the basis for energy policies
  Panicked energy strategies are force feeding inherently deficient wind & solar
  Need intellectually honest life-cycle cost-versus-benefit analysis; financial & ecological
  Environmental virtue signaling versus real global impacts
Data shows bending global CO2 emissions & concentration curves is likely a longer-term prospect
  Energy poverty is human poverty; we need more global energy, not less
  Greenhouse effect saturates with increasing CO2 concentration
“All of the above” sounds nice but . . .
  Overbuilding wind, solar & batteries diverts intellectual & financial capital from reliable solutions
How about “always the best” reliable, small-footprint, low or no CO2 technologies

## Slide 73: Can We Please Find Common Ground
“How about an energy future of abundance and human flourishing, not one based on unprecedented land grabs, intermittency, variability, and scarcity.”
“I know it might seem like a long shot, but we must create a “safe space” for natural gas to be put back on the table in Washington and Oregon.”
Natural-Gas-to-Nuclear (N2N) is worth considering